J8CM Assembly Language Compiler

A menu driven compiler for Jay's 8-bit Computer Model.

Documentation conventions:

Instruction mnemonics are in caps as required by compiler.

(arg) indicates the instruction or pseudoinstruction requires an operand(argument).

(#arg) indicates the instruction or pseudoinstruction requires a number as its argument.

 Psuedo-instructions:
EQU(#arg)	- Equals statement. Compiler constant, declares a label is equal to arg.
DAT(#arg)	- Reserves a memory location for data. Initializes location to value of arg.
ORG(#arg)	- Declares starting memory location for code that follows.
END(arg)	- Tells compiler to stop compiling. Place at end of source code. Arg is required but not used.
*	- Comments When the compiler encounters an "*" it ignores all text that follows, until it	encounters another "*".
:	- Label declarations require a ":". Labels can be no longer than 5 characters.

Instruction Format:

7	6	5	4	3	2	1	0
R	Address Mode		Op Code

R – Register:
If set to 0, select X register. If set to 1, select Y register. (Register address modes only)

Address Mode:
00 – Memory direct
01 – Memory indirect
10 – Register direct
11 – Register indirect

 Instruction Set:

Op Code	Mnemonic	ML Code (decimal)	# Args	Description
00010	ADD	2	1	Add the contents of the memory location pointed to by arg to the accumulator.
11001	AND	25	1	Bit-wise AND. ACC & operand
01111	ASL	15	0	Arithmetic Shift Left. ACC * 2
10000	ASR	16	0	Arithmetic Shift Right. Arithmetically shifts the accumulator to the right one bit. (preserves the sign bit) ACC / 2
11101	CLR	29	0	Clears the accumulator
11110	CMP	30	1	Compares the ACC to operand
01011	DEC	11	0	Decrement the accumulator.
01100	GSB	12	1	Go to Subroutine. Performs a subroutine starting at the memory location specified by arg. A RTN statement is required at the end of the subroutine.
01001	HLT	9	1	Halt. Program halt, arg is copied into the program counter.
01010	INC	10	0	Increment the contents of the accumulator
00000	INP	0	1	Input one byte from I/O to the memory location specified by arg.
00110	JMP	6	1	Jump to the memory location specified by arg.
00111	JNG	7	1	Jump to the memory location specified by arg if the accumulator is negative.
01000	JZR	8	1	Jump to operand if PSW Z flag is set.
10011	LDX	19	1	Loads the X register with the contents of the memory location specified by arg.
10100	LDY	20	1	Loads the Y register with the contents of the memory location specified by arg.
00100	LOD	4	1	Loads the accumulator with the contents of the memory location specified by arg.
01110	LSR	14	0	Logical Shift Right the accumulator one bit.
11010	OR	26	1
00001	OUT	1	1	Output the contents of the memory location specified by arg to I/O.
10010	POP	18	0	Remove the top item from the stack and place it in the accumulator.
10001	PSH	17	0	Push the contents of the accumulator onto the stack.
10111	ROL	23	0
11000	ROR	24	0
01101	RTN	13	0	Return from subroutine.
00101	STO	5	1	Stores the contents of the accumulator in the memory location specified by arg.
10101	STX	21	1
10110	STY	22	1
00011	SUB	3	1	Subtract the contents of the memory location specified by arg from the accumulator. The result is left in the accumulator.
11011	XOR	27	1

 The Compiler

  The source file must have a ".asm" extender. When a filename is entered the ".asm" extender is appended automatically.

 The compiler looks for a file named "xinstr.set". This file contains the instruction set mnemonics and machine language equivalents. "xinstr.set" is read into a binary search tree.

Pass 1
- Places labels and their associated values into a binary search tree or symbol tree. Syntax and error checking. If no errors are found pass 2 is enabled. The symbol tree is saved using the source filename with a ".sym" extender.
- Creates file <error.log> when compiler is called. Any existing error log file is deleted.

Pass 2
- Creates an integer file using the source filename and an ".obj" extender. The object file contains the address count, ML instruction code, and the ML instruction argument.
- Outputs to the screen a line by line comparison of the object and source files. saves in file using filename and ".sum" extender.
- Creates a bootable file using object filename and an ".ldr" extender.

File Summary

a:error.log - Created during Pass 1. Contains Pass 1 errors.
Deleted when compiler is called.
a:xinstr.set - Created with <opcoedit.exe>. Contains mnemonic to ML data.
Instruction tree is created with <instr.set> before the
main menu is displayed.
<filename>.asm – Assembler (text) source file.
<filename>.sym - Created from <filename>.src by Pass 1. Contains the
symbol table data.
<filename>.obj - Created from <filename>.src by Pass 2. Contains the
address count, ML instruction code, and the
ML instruction argument.
<filename>.sum - Created from <filename>.src by Pass 2. Contains summary
data. Line by line comparison of object and source codes.
<filename>.ldr - Created from <filename>.obj at the end of Pass 2.
Contains an integer listing for a boot and execute
file.

J8CM AL Compiler Bugs (unconfirmed since port to gcc)

 Pass 1 errors if labels contain instruction mnemonic substrings. (i.e. if STOP is used as a label it will produce a pass 1 error - illegal label.)

The STO instruction produces a match when the instruction tree is searched, generating the error.

The summary display after pass 2 does not correctly display the address counter.

 Post compiler view file routines are unreliable with anything but small source files. Larger files can be viewed with a text editor.

Although the symbol table and instruction set are loaded into binary search trees the compiler program does not balance the trees. An unbalanced tree is less efficient. In fact, the instruction set file editor writes the instruction set file by printing an in-order traversal of the tree it created. This results in the instructions being written in alphabetical order. When the compiler inserts the data into its search tree it will always select the right node because the key of the node read will always
be less than the keys of nodes already inserted into the tree. Probably the best solution to this problem is to not worry about the symbol table, but implement code to balance the instruction set tree in the instruction set file editor. The instruction set file should then be written using a level-order traversal of the instruction tree.

*********************************************

 j8_oped.cpp
Instruction set file editor for J8 AL Compiler.

The file "xinstr.set" contains the instruction set translations, this utility is used to create and/or edit that file. For instance, if you prefer the mnemonic CAL to GSB to call a subroutine you can use this utility to change it.

When "j8_oped.exe" is run user is presented with a main menu.

1. new rule tree - initializes the rule tree. Any existing tree in memory is destroyed.
2. add rules
3. delete rules
4. view rules
5. search rule
6. rule I/O - read or write instruction set file

When the add rule option is selected user is:

1. Prompted to enter op-code - enter 3 letter mnemonic code
2. Prompted to enter op-code - decimal ML value
3. Prompted to enter number of arguments - enter 0 or 1
4. Prompted to add another rule - enter y or n

*********************************

Test Files

test.src	- a file with assorted syntax errors.
test1.src - a file with assorted syntax errors.
test2.src - a file with assorted syntax errors.

addition.src - source code from Simple Computer handout.
multiply.src - source code to take a 2-digit number and multiply it by a 1-digit number.