j8cm_alc.doc
 Jay Babel
 cmsc265
 Spring 1995

J8CM Assembly Language Compiler

 A menu driven compiler for Jay's 8-bit Computer Model.

 Assembly Language Source Code

Psuedoinstructions are as per Simple Computer handout. Comments are handled slightly different. Comments are placed between asterisks. When the compiler encounters an "*" it ignores all text that follows, until it encounters another "*".
Label declarations require a ":". Labels can be no longer than 5 characters.

 Psuedoinstructions:
EQU
DAT
ORG
END
*
:

Machine instructions are as per Simple Computer handout where applicable. The J8CM has a larger instruction set than Simple Computer. (Simple Computer was the tool used in the computer architecture class)

 Instruction Set:

Mnemonic	ML Code (decimal)	# Args
ADD	2	1
ASR	16	0
DEC	11	0
GSB	12	1
HLT	9	1
INC	10	0
INP	0	1
JMP	6	1
JNG	7	1
LOD	4	1
LSL	15	0
LSR	14	0
OUT	1	1
POP	18	0
PSH	17	0
RTN	13	0
STO	5	1
SUB	3	1

 The Compiler

  The source file must have a ".asm" extender. When a filename is entered
 the ".asm" extender is appended automatically.

 The compiler looks for a file on drive a: named "xinstr.set". This file
 contains the instruction set mnemonics and their machine language
 equivalents.
 "xinstr.set" is read into a binary search tree.

 Pass 1 places labels and their associated values into a
 binary search tree or symbol tree. Syntax and error checking.
 If no errors are found pass 2 is enabled.

 The symbol tree is saved using the source filename with a ".sym" extender.
 Creates file <error.log> when compiler is called any existing error log
 file is deleted.

Pass 2
 1. creates an integer file using the source filename and an ".obj" extender.
The object file contains the address count, ML instruction code, and
the ML instruction argument.
 2. outputs to the screen a line by line comparison of the object and source
files. saves in file using filename and ".sum" extender.
 3. creates a bootable file using object filename and an ".ldr" extender.

File Summary

a:error.log - Created during Pass 1. Contains Pass 1 errors.
Deleted when compiler is called.
a:xinstr.set - Created with <opcoedit.exe>. Contains mnemonic to ML data.
Instruction tree is created with <instr.set> before the
main menu is displayed.
<filename>.asm – Assembler (text) source file.
<filename>.sym - Created from <filename>.src by Pass 1. Contains the
symbol table data.
<filename>.obj - Created from <filename>.src by Pass 2. Contains the
address count, ML instruction code, and the
ML instruction argument.
<filename>.sum - Created from <filename>.src by Pass 2. Contains summary
data. Line by line comparison of object and source codes.
<filename>.ldr - Created from <filename>.obj at the end of Pass 2.
Contains an integer listing for a boot and execute
file.

 J8CM AL Compiler Bugs

 Pass 1 errors if labels contain instruction mnemonic substrings. (i.e.
if STOP is used as a label it will produce a pass 1 error - illegal label.
The STO instruction produces a match when the instruction tree is searched,
generating the error.)

 The summary display after pass 2 does not correctly display the address
counter.

 Post compiler view file routines are unreliable with anything but small
source files. Larger files can be viewed with a text editor.

  Although the symbol table and instruction set are loaded into binary
search trees the compiler program does not balance the trees. An unbalanced
tree is less efficient. In fact, the instruction set file editor writes
the instruction set file by printing an in-order traversal of the tree
it created. This results in the instructions being written in alphabetical
order. When the compiler inserts the data into its search tree it will
always select the right node because the key of the node read will always
be less than the keys of nodes already inserted into the tree. Probably
the best solution to this problem is to not worry about the symbol table,
but implement code to balance the instruction set tree in the instruction
set file editor. The instruction set file should then be written using a
level-order traversal of the instruction tree.

*********************************************

 j8_oped.cpp
Instruction set file editor for J8 AL Compiler.
The file "a:xinstr.set" contains the instruction set translations,
 this utility is used to create and/or edit that file. For instance, if
 you prefer the mnemonic CAL to GSB to call a subroutine you can use
 this utility to change it.

When "j8_oped.exe" is run user is presented with a main menu.
1. new rule tree - initializes the rule tree. Any existing tree
in memory is destroyed.
2. add rules
3. delete rules
4. view rules
5. search rule
6. rule I/O - read or write instruction set file

When add rule option is selected user is:
 *Prompted to enter op-code - enter 3 letter mnemonic code
 *Prompted to enter op-code - decimal ML value
 *Prompted to enter number of arguments - enter 0 or 1
 *Prompted to add another rule - enter y or n

*********************************

Test Files

test.src	- a file with assorted syntax errors.
test1.src - a file with assorted syntax errors.
test2.src - a file with assorted syntax errors.

addition.src - source code from Simple Computer handout.
multiply.src - source code to take a 2-digit number and multiply
it by a 1-digit number.