J8CM Assembly Language Programmer’s Guide

Documentation Conventions

Instruction mnemonics are in caps as required by compiler.

[arg] indicates the instruction or pseudoinstruction requires an operand(argument).

[#arg] indicates the instruction or pseudoinstruction requires a number as its argument.

& - logical AND operator

|| - logical OR operator

! - logical NOT operator

M - memory location

R - general purpose register X or Y

Brackets are used to group operations in the XOR instruction to avoid confusion with address indirection.

Psuedoinstructions

* - Remark. When the compiler encounters a * it will ignore all text that follows until another * is encountered.
[arg]: - Label. Declares arg as a label.

DAT [#arg] - Reserves a memory location for data. Initializes location to value of arg.

END [arg] - Tells compiler to stop compiling. Place at end of source code. Arg is required but not used.

EQU [#arg] - Equals statement. Compiler constant, declares a label is equal to arg.

ORG [#arg] - Declares starting memory location for code that follows.

Address Mode Operators
 [arg] - Default address mode is memory direct.
([arg]) - Parenthesis indicate indirect address mode.
/[arg] - Register addressing mode. Where [arg] is either X or Y.
(/[arg]) - Register indirect addressing mode.

Instruction Set

Data Transfer Instructions

INP	[arg] PC f PC + 1; M f I/O
([arg])	PC f PC + 1; (M) f I/O
(/[arg]) (R) f I/O
Input one byte from I/O to the memory location specified by arg.
Flags:	Unaffected.

LDX	[arg] PC f PC + 1; XREG f M
([arg])	PC f PC + 1; XREG f (M)
/[arg]	XREG f R
(/[arg]) XREG f (R)
Loads the X register with the contents specified by arg.
Flags:	Z - Set to 1 if XREG = 0. Cleared otherwise.
N - Set to 1 if XREG < 0. Cleared otherwise.

LDY	[arg]	PC f PC + 1; YREG f M
([arg])	PC f PC + 1; YREG f (M)
/[arg]	YREG f R
(/[arg]) YREG f (R)
Loads the Y register with the contents specified by arg.
Flags:	Z - Set to 1 if YREG = 0. Cleared otherwise.
 N - Set to 1 if YREG < 0. Cleared otherwise.

LOD	[arg]	PC f PC + 1; ACC f M
([arg])	PC f PC + 1; ACC f (M)
/[arg]	ACC f R
(/[arg])	ACC f (R) Loads the accumulator with the contents of the memory location specified by arg.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC << 0. Cleared otherwise.

OUT [arg] PC f PC + 1; I/O f M
([arg])	PC f PC + 1; I/O f (M)
(/[arg]) I/O f (R)
Output the contents of the memory location specified by arg to I/O.
Flags:	Unaffected.

POP	ACC f (SP); SP f SP + 1
Remove the top item from the stack and place it in the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.

PSH	SP f SP - 1; (SP) f ACC
 Push the contents of the accumulator onto the stack.
Flags:	Unaffected.

STO	[arg] PC f PC + 1; M f ACC
([arg])	PC f PC + 1; (M) f ACC
 /[arg]	R f ACC
(/[arg]) (R) f ACC
Stores the contents of the accumulator in the memory location specified by arg.
Flags:	Unaffected.

STX [arg] PC f PC + 1; M f XREG
([arg])	PC f PC + 1; (M) f XREG
/[arg]	R f XREG
(/[arg]) (R) f XREG
Stores the contents of the X register in the memory location specified by arg.
Flags:	Unaffected.

STY [arg] PC f PC + 1; M f YREG
([arg])	PC f PC + 1; (M) f YREG
/[arg]	R f YREG
(/[arg]) (R) f YREG
Stores the contents of the Y register in the memory location specified by arg.
Flags:	Unaffected.

Arithmetic/Logic Instructions

ADD [arg] PC f PC + 1; ACC f ACC + M
([arg])	PC f PC + 1; ACC f ACC + (M)
/[arg]	ACC f ACC + R
 (/[arg])	ACC f ACC + (R)
Add the operand to the accumulator, leaving the result in the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Set if operation results in a carry. Cleared otherwise.

ASR	ACC f ACC / 2
Arithmetic Shift Right. Arithmetically shifts the accumulator to the right one bit. (preserves the sign bit)
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
 N - Set to 1 if ACC < 0. Cleared otherwise.

ASL	ACC f ACC * 2
Arithmetic Shift Left. Arithmetically shifts the accumulator to the left one bit.
Accumulator bit 0 is set to 0.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Accumulator MSB is shifted into the C flag.

AND [arg] PC f PC + 1; ACC f ACC & M
([arg]) PC f PC + 1; ACC f ACC & (M)
/[arg]	ACC f ACC & R
(/[arg])	ACC f ACC & (R)
Bit-wise AND of operand to accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
V – Cleared.

DEC	ACC f ACC – 1
Decrement the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Set if operation results in a carry. Cleared otherwise.

INC	ACC f ACC + 1
Increment the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Set if operation results in a carry. Cleared otherwise.

LSR Logical shift the accumulator right one bit. The MSB is loaded with 0.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 0.

NOT [arg] PC f PC + 1; ACC f !M
([arg])	PC f PC + 1; ACC f !(M)
/[arg]	ACC f !R
(/[arg]) ACC f !(R)
Performs a bit-wise NOT of operand and places the result in the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
V - Cleared.

OR [arg] PC f PC + 1; ACC f ACC || M
([arg])	PC f PC + 1; ACC f ACC || (M)
/[arg]	ACC f ACC || R
(/[arg])	ACC f ACC || (R)
 Bit-wise OR of operand to accumulator.
 Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
 N - Set to 1 if ACC << 0. Cleared otherwise.
 V - Cleared.

ROR	Rotate all accumulator bits right one place. The low-order bit is placed in
C and the previous contents of C are loaded into the high-order bit.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Loaded with low-order bit of the accumulator.
V - Loaded with exclusive OR of N and C.

ROL Rotate all accumulator bits left one place. The high-order bit is placed in
C and the previous contents of C are loaded into the low-order bit.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Loaded with high-order bit of the accumulator.
V - Loaded with exclusive OR of N and C.

SUB [arg] PC f PC + 1; ACC f ACC – M
([arg])	PC f PC + 1; ACC f ACC – (M)
/[arg]	ACC f ACC – R
(/[arg])	ACC f ACC - (R)
Subtract the operand from the accumulator, leaving the result in the accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
C - Set if operation results in a carry. Cleared otherwise.

XOR [arg] PC f PC + 1; ACC f [ACC || M] & ![ACC & M]
([arg])	PC f PC + 1; ACC f [ACC || (M)] & ![ACC & (M)]
/[arg]	ACC f [ACC || R] & ![ACC & R]
(/[arg]) ACC f [ACC || (R)] & ![ACC & (R)]
 Bit-wise exclusive OR of operand to accumulator.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.
V - Cleared.

Control Instructions

GSB [arg] SP f SP - 1; PC f PC + 1; (SP) f PC; PC f M
Go to Subroutine. Performs a subroutine starting at the memory location specified by arg. A RTN statement is required at the end of the subroutine.
Flags:	Unaffected.

HLT [arg]	PC f M
Halt. Program halt, arg is copied into the program counter.
Flags:	Unaffected.

JMP [arg]	PC f PC + 1; PC f M
Jump to the memory location specified by arg.
Flags:	Unaffected.

RTN	PC f (SP); SP f SP + 1
Return from subroutine.
Flags:	Unaffected.

Conversion Instructions

CLR	ACC f 0
Clears the accumulator.
Flags:	Z - Set to 1.
N – Cleared.
C – Cleared.
V – Cleared.

NEG	ACC f ACC * -1
Multiplies the accumulator by -1.
Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.
N - Set to 1 if ACC < 0. Cleared otherwise.

Conditional Instructions

CMP [arg] PC f PC + 1; ACC – M
([arg])	PC f PC + 1; ACC – (M)
/[arg]	ACC – R
(/[arg])	ACC - (R)
Compare the operand to the accumulator.
Flags:	Z - Set to 1 if ACC = operand. Cleared otherwise.
N - Set to 1 if ACC < operand. Cleared otherwise.

JNG [arg] PC f PC + 1; PC f M
Jump to the memory location specified by arg if the N flag is set.
Flags:	Unaffected.

JZR [arg] PC f PC + 1; PC f M
Jump to the memory location specified by arg if the Z flag is set.
Flags:	Unaffected.