Demo: Load the accumulator – all modes

There are six methods by which the accumulator can be loaded:
- Memory direct – loads data from the memory location specified in the argument
- Memory indirect – loads data from the memory location specified in the memory location specified in the argument.
- X Register direct – loads the contents of the X register directly into the accumulator
- X register indirect – loads the accumulator with the contents of the memory location specified by the contents of the X register
- Y Register direct – loads the contents of the Y register directly into the accumulator
- Y register indirect – loads the accumulator with the contents of the memory location specified by the contents of the Y register

010: 00010011	load x reg memory direct: expected contents of x reg 00100000 (032)
011: 01000000	(064)
012: 00010100	load y reg memory direct: expected contents of y reg 00111000 (056)
013: 01000001	(065)
014: 00000100	load accumulator memory direct : expected contents of accumulator 10101010
015: 01000010	(066)
016: 00011101	clear accumulator
017: 00100100	load accumulator memory indirect : expected contents of accumulator 11111111
018: 01000011	(067)
019: 00011101	clear accumulator
020: 01000100	load accumulator x reg direct : expected contents of accumulator 00100000
021: 00011101	clear accumulator
022: 01100100	load accumulator x reg indirect : expected contents of accumulator 11110000
023: 00011101	clear accumulator
024: 11000100	load accumulator y reg direct : expected contents of accumulator 00111000
025: 00011101	clear accumulator
026: 11100100	load accumulator y reg indirect : expected contents of accumulator 00001111
027: 00011101	clear accumulator
028: 00001001	halt
029: 00001010

032: 11110000	bit pattern
056: 00001111	bit pattern

064: 00100000	(032)
065: 00111000	(056)
066: 10101010	bit pattern
067: 10000000	(128)

128: 11111111	bit pattern