// j8_alpg.doc

J8CM Assembly Language Programmer's Guide

 Documentation conventions:

Instruction mnemonics are in caps as required by compiler.

(arg) indicates the instruction or pseudoinstruction requires
 an operand(argument).

(#arg) indicates the instruction or pseudoinstruction requires
 a number as its argument.

 Psuedoinstructions

 *
Remark. When the compiler encounters a * it will ignore all text that
follows until another * is encountered.

 (arg):
Label. Declares arg as a label.

 DAT (#arg)
Reserves a memory location for data. Initializes location to value of
arg.

 END (arg)
Tells compiler to stop compiling. Place at end of source code.
Arg is required but not used.

 EQU (#arg)
Equals statement. Compiler constant, declares a label is equal to
arg.

 ORG (#arg)
Declares starting memory location for code that follows.

 Instruction Set

 ADD (arg)
Add the contents of the memory location pointed to by arg to
the accumulator.

 ASR
Arithmetic Shift Right. Arithmetically shifts the accumulator to the
right one bit. (preserves the sign bit)

 DEC
Decrement the accumulator.

 GSB (arg)
Go to Subroutine. Performs a subroutine starting at the memory
location specified by arg. A RTN statement is required at the end
of the subroutine.

 HLT (arg)
Halt. Program halt, arg is copied into the program counter.

 INC
Increment the accumulator.

 INP (arg)
Input one byte from I/O to the memory location specified by
arg.

 JMP (arg)
Jump to the memory location specified by arg.

 JNG (arg)
Jump to the memory location specified by arg if the accumulator
is negative.

 LOD (arg)
Loads the accumulator with the contents of the memory location
specified by arg.

 LSL
Logical Shift Left the accumulator one bit.

 LSR
Logical Shift Right the accumulator one bit.

 OUT (arg)
Output the contents of the memory location specified by arg to I/O.

 POP
Remove the top item from the stack and place it in the accumulator.

 PSH
Push the contents of the accumulator onto the stack.

 RTN
Return from subroutine.

 STO (arg)
Stores the contents of the accumulator in the memory location
specified by arg.

 SUB (arg)
Subtract the contents of the memory location specified by arg from
the accumulator. The result is left in the accumulator.