<P14>J8CM Assembly Language Programmer’s Guide<P255>
 Documentation Conventions
Instruction mnemonics are in caps as required by compiler.
[arg]   indicates the instruction or pseudoinstruction requires an operand(argument).
[#arg]  indicates the instruction or pseudoinstruction requires a number as its argument.
& - logical AND operator
|| - logical OR operator
! - logical NOT operator
M - memory location
R - general purpose register X or Y
Brackets are used to group operations in the XOR instruction to avoid confusion with address	indirection.
Psuedoinstructions
* - Remark. When the compiler encounters a * it will ignore all text that follows until another *	is encountered.
[arg]: - Label. Declares arg as a label.
DAT [#arg] - Reserves a memory location for data. Initializes location to value of arg.
END [arg] - Tells compiler to stop compiling. Place at end of source code.  Arg is required but	        	        not used.
EQU [#arg] - Equals statement. Compiler constant, declares a label is equal to arg.
ORG [#arg] - Declares starting memory location for code that follows.
<$TBrkPage=B>Address Mode Operators
[arg] - Default address mode is memory direct.<R>	([arg]) - Parenthesis indicate indirect address mode.<R>	/[arg] -  Register addressing mode. Where [arg] is either X or Y.<R>	(/[arg]) - Register indirect addressing mode.
<$TBrkPage=B> Instruction Set
Data Transfer Instructions<D>
INP<D> [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; M <D><F"Symbol">¬<W0><F255> I/O<R>	([arg])	 PC <D><F"Symbol">¬<W0><F255> PC + 1; (M) <D><F"Symbol">¬<W0><F255> I/O<R>	(/[arg])  (R) <D><F"Symbol">¬<W0><F255> I/O<R>	Input one byte from I/O to the memory location specified by arg.<R>	Flags:	Unaffected.
LDX [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; XREG <D><F"Symbol">¬<F255> M<R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; XREG <D><F"Symbol">¬<F255>  (M)<R>	/[arg]	XREG <F"Symbol">¬<F255> R<R>	(/[arg])  XREG <F"Symbol">¬<F255> (R)<R>	Loads the X register with the contents specified by arg.<R>	Flags:	Z - Set to 1 if XREG = 0. Cleared otherwise.<R>	N - Set to 1 if XREG << 0. Cleared otherwise.<R><R>	LDY [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; YREG <D><F"Symbol">¬<F255> M<R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; YREG <D><F"Symbol">¬<F255>  (M)<R>	/[arg]	YREG <F"Symbol">¬<F255> R<R>	(/[arg])  YREG <F"Symbol">¬<F255> (R)<R>	Loads the Y register with the contents specified by arg.<R>	Flags:	Z - Set to 1 if YREG = 0. Cleared otherwise.<R>	N - Set to 1 if YREG << 0. Cleared otherwise.
LOD [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; ACC <D><F"Symbol">¬<F255> M<R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; ACC <D><F"Symbol">¬<F255>  (M)<R>	/[arg]	ACC <F"Symbol">¬<F255> R<R>	(/[arg])  ACC <F"Symbol">¬<F255> (R)<R>	Loads the accumulator with the contents of the memory location specified by arg.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.
OUT [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; I/O <D><F"Symbol">¬<W0><F255> M<R>	([arg])	 PC <D><F"Symbol">¬<W0><F255> PC + 1; I/O <D><F"Symbol">¬<W0><F255> (M)<R>	(/[arg])  I/O <D><F"Symbol">¬<W0><F255> (R)<R>	Output the contents of the memory location specified by arg to I/O.<R>	Flags:	Unaffected.
<$TEfWeight=4;BrkPage=B>	POP	ACC <F"Symbol">¬<F255> (SP); SP <F"Symbol">¬<F255> SP + 1<R>	Remove the top item from the stack and place it in the accumulator.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.
PSH	SP <F"Symbol">¬<F255> SP - 1; (SP) <F"Symbol">¬<F255> ACC<R>	Push the contents of the accumulator onto the stack.<R>	Flags:	Unaffected.
STO [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; M <D><F"Symbol">¬<F255> ACC <R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; (M) <D><F"Symbol">¬<F255> ACC <R>	/[arg]	R <F"Symbol">¬<F255> ACC <R>	(/[arg])  (R) <F"Symbol">¬<F255> ACC <R>	Stores the contents of the accumulator in the memory location specified by arg.<R>	Flags:	Unaffected.
STX [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; M <D><F"Symbol">¬<F255> XREG <R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; (M) <D><F"Symbol">¬<F255> XREG <R>	/[arg]	R <F"Symbol">¬<F255> XREG<R>	(/[arg])  (R) <F"Symbol">¬<F255> XREG <R>	Stores the contents of the X register in the memory location specified by arg.<R>	Flags:	Unaffected.
STY [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; M <D><F"Symbol">¬<F255> YREG <R>	([arg])	PC <F"Symbol">¬<W0><F255> PC + 1; (M) <D><F"Symbol">¬<F255> YREG<R>	/[arg]	R <F"Symbol">¬<F255> YREG<R>	(/[arg])  (R) <F"Symbol">¬<F255> YREG <R>	Stores the contents of the Y register in the memory location specified by arg.<R>	Flags:	Unaffected.
Arithmetic/Logic Instructions<D>
ADD [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1; ACC <D><F"Symbol">¬<F255> ACC + M<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1; ACC <D><F"Symbol">¬<F255> ACC + (M)<R>	/[arg]	 ACC <F"Symbol">¬<F255>  ACC + R<R>	(/[arg])	 ACC <F"Symbol">¬<F255>  ACC + (R)<R>	Add the operand to the accumulator, leaving the result in the accumulator.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC  << 0. Cleared otherwise.<R>	C - Set if operation results in a carry. Cleared otherwise.
<$TEfWeight=4;BrkPage=B>	 ASR	<M>ACC<M><F"Symbol"> ¬<D><F255> ACC / 2<R>	Arithmetic Shift Right. Arithmetically shifts the accumulator to the right one bit. (preserves the	sign bit)<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC  << 0. Cleared otherwise.
 ASL	<M>ACC<M><F"Symbol"> ¬<D><F255> ACC * 2<R>	Arithmetic Shift Left. Arithmetically shifts the accumulator to the left one bit.  Accumulator bit 0	is set to 0.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Accumulator MSB is shifted into the C flag.
AND [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC <F"Symbol">&<F255> M<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC & (M)<R>	/[arg]	 ACC <F"Symbol">¬<F255>  ACC & R<R>	(/[arg])	 ACC <F"Symbol">¬<F255>  ACC & (R)<R>	Bit-wise AND of operand to accumulator.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	V - Cleared.
DEC	ACC <D><F"Symbol">¬<F255> ACC - 1<R>	Decrement the accumulator.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Set if operation results in a carry. Cleared otherwise.
INC	ACC <D><F"Symbol">¬<F255> ACC + 1<R>	Increment the accumulator.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Set if operation results in a carry. Cleared otherwise.
LSR<R>	Logical shift the accumulator right one bit. The MSB is loaded with 0.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 0.<R><R>	NOT [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> !M<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> !(M)<R>	/[arg]	 ACC <F"Symbol">¬<F255>  !R<R>	(/[arg])	 ACC <F"Symbol">¬<F255>  !(R)<R>	Performs a bit-wise NOT of operand and places the result in the accumulator.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	V - Cleared.<R><R>	OR [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC || M<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC || (M)<R>	/[arg]	 ACC <F"Symbol">¬<F255>  ACC || R<R>	(/[arg])	 ACC <F"Symbol">¬<F255>  ACC || (R)<R>	Bit-wise OR of operand to accumulator.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	V - Cleared.<R><R>	ROR<R>	Rotate all accumulator bits right one place.  The low-order bit is placed in C and the previous	contents of C are loaded into the high-order bit.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Loaded with low-order bit of the accumulator.<R>	V - Loaded with exclusive OR of  N and C.<R><R>	ROL<R>	Rotate all accumulator bits left one place.  The high-order bit is placed in C and the previous	contents of C are loaded into the low-order bit.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Loaded with high-order bit of the accumulator.<R>	V - Loaded with exclusive OR of  N and C.
SUB [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC - M<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> ACC - (M)<R>	/[arg]	 ACC <F"Symbol">¬<F255>  ACC - R<R>	(/[arg])	 ACC <F"Symbol">¬<F255>  ACC - (R)<R>	Subtract  the operand from the accumulator, leaving the result in the accumulator..<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	C - Set if operation results in a carry. Cleared otherwise.
<W0>	<D>XOR<D> [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> [ACC || M] & ![ACC & M]<R>	([arg])	 PC <F"Symbol">¬<W0><F255> PC + 1;  ACC <D><F"Symbol">¬<F255> [ACC || (M)] & ![ACC & (M)]<R>	/[arg]	 ACC <F"Symbol">¬<F255>  [ACC || R] & ![ACC & R]<R>	(/[arg])  ACC <F"Symbol">¬<F255>  [ACC || (R)] & ![ACC & (R)]<R>	Bit-wise exclusive OR of operand to accumulator.<R>	Flags:	Z - Set to 1 if ACC  = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R>	V - Cleared.
Control Instructions<D>
GSB [arg]	 SP <F"Symbol">¬<F255> SP - 1; PC <F"Symbol">¬<W0><F255> PC + 1;  (SP) <D><F"Symbol">¬<F255>  PC; PC <F"Symbol">¬<F255> M<R>	Go to Subroutine. Performs a subroutine starting at the memory location specified by arg. A	RTN statement is required at the end of the subroutine.<R>	Flags:	Unaffected.
HLT [arg]	PC <F"Symbol">¬<F255> M<R>	Halt. Program halt, arg is copied into the program counter.<R>	Flags:	Unaffected.
JMP [arg]	PC <F"Symbol">¬<W0><F255> PC + 1; PC <D><F"Symbol">¬<F255> M<R>	Jump to the memory location specified by arg.<R>	Flags:	Unaffected.
RTN	PC <D><F"Symbol">¬<F255>  (SP); SP <F"Symbol">¬<F255> <F"Symbol">ÿ<F255>SP + 1<R>	Return from subroutine.<R>	Flags:	Unaffected.
Conversion Instructions<D>
CLR	ACC <F"Symbol">¬<F255> 0<R>	Clears the accumulator.<R>	Flags:	Z - Set to 1.<R>	N -  Cleared.<R>	C - Cleared.<R>	V - Cleared.<R><R>	NEG	ACC <F"Symbol">¬<F255> ACC * -1<R>	Multiplies the accumulator by -1.<R>	Flags:	Z - Set to 1 if ACC = 0. Cleared otherwise.<R>	N - Set to 1 if ACC << 0. Cleared otherwise.<R><R>Conditional Instructions<D>
CMP [arg]	 PC <F"Symbol">¬<W0><F255> PC + 1; ACC - M<R>	([arg])	 PC <D><F"Symbol">¬<W0><F255> PC + 1; ACC - (M)<R>	/[arg]	 ACC - R<R>	(/[arg])	 ACC - (R)<R>	Compare  the operand to  the accumulator.<R>	Flags:	Z - Set to 1 if ACC = operand. Cleared otherwise.<R>	N - Set to 1 if ACC << operand. Cleared otherwise.
<W0>	<D>JNG<D> [arg]  PC <F"Symbol">¬<W0><F255> PC + 1; PC <D><F"Symbol">¬<F255> M<R>	Jump to the memory location specified by arg if the N flag is set.<R>	Flags:	Unaffected.
JPZ [arg]  PC <F"Symbol">¬<W0><F255> PC + 1; PC <D><F"Symbol">¬<F255> M<R>	Jump to the memory location specified by arg if the Z flag is set.<R>	Flags:	Unaffected.