J8CM Front Panel Quick Reference

J8CM Front Panel

 PC	IR	SP
 -----------------------	-----------------------	----------------------
  0 0 0 0 0 0 0 0	0 0 0 0 0 0 0 0	0 0 0 0 0 0 0 0
 -----------------------	-----------------------	----------------------

  MAR	PSW
  -----------------------	-----------------------
   0 0 0 0 0 0 0 0	0 0 0 0 0 0 0 0
  -----------------------	-----------------------

  Accumulator
  -----------------------
   0 0 0 0 0 0 0 0
  -----------------------

  X Register	Y Register	cycle
  -----------------------	-----------------------	---------
   0 0 0 0 0 0 0 0	0 0 0 0 0 0 0 0	fetch
  -----------------------	-----------------------	execute
    p -set PC, f -fetch, e -execute, s -step, r -run, c -clear
        x -exit front panel

PC – Program Counter. Contains the memory address of the next instruction or argument (fetched)

IR – Instruction Register

SP – Stack Pointer. Set to 255 (top of memory) when the stack is initialized (first item is placed on the stack), set to 0 when the stack is empty.

MAR – Memory Address Register: Contains the next memory address to be read from

PSW – Processor Status Word: The PSW consists of four flags:
c_flag - Cycle flag. PSW[8]. Set to zero after a fetch cycle is completed. Set to one after an execute cycle is completed. Initially the cycle flag is undefined and is not displayed on the front panel.
v_flag - Overflow flag. PSW[7]. Not used.
FLG.v_flag = ((FLG.n_flag || FLG.c_flag) && !(FLG.n_flag && FLG.c_flag));
n_flag - Negative flag. PSW[6]. The n-flag is set to one when bit 8 of the accumulator is set to one.
z_flag - Zero flag. PSW[5]The z_flag is set to one when the contents of the accumulator equals zero.

Accumulator - The J8CM is an accumulator based CPU. All arithmetic and logic operations operate on the accumulator, as do the conversion and stack operators.

X Register - General purpose register

Y Register - General purpose register