J8CM Technical Data

<Architecture Diagram goes here>

Accumulator - The J8CM is an accumulator based CPU. All arithmetic and logic operations operate on the accumulator, as do the conversion and stack operators.

ALU - Arithmetic Logic Unit. Contains complementor, shifter and temporary accumulator. Sets, clears and senses CPU flags.

Control - Interprets IR and issues control signals. To eliminate clutter, a single line to the internal CPU bus serves to represent control of data flow within the CPU. The control unit interfaces directly with the 2 bit external control bus.

IR- Instruction Register.

Flags
C - Carry flag. The c_flag is set when an operation results in a carry.
V - Overflow flag. The v_flag is set when an operation results in an overflow.
N - Negative flag. The n-flag is set to one when the result of an operation is negative.
Z - Zero flag. The z_flag is set to one when the contents of an operation equals zero.

MAR - Memory Address Register.

MBR - Memory Buffer Register.

PC - Program Counter. Incremented by 1 if instruction has no operand, by 2 otherwise.

PSW - Processor Status Word. The CPU flags are copied into the high order bits. The PSW is displayed on the front panel, and is otherwise not used. The four CPU flags are copied into the high order bits of the PSW as follows*:

PSW bit 7 = C
PSW bit 6 = V
PSW bit 5 = N
PSW bit 4 = Z

SP - Stack Pointer. Set to 255 (top of memory) when the stack is initialized (first item is placed on the stack), set to 0 when the stack is empty.

XREG/YREG - General purpose CPU registers. The instruction set includes load and store op codes for these registers.

Memory addressing modes supported:

Memory Direct
Memory Indirect
Register Direct
Register Indirect

The Instruction Cycle
16 bit word - 8-bit instruction, 8-bit operand.<R>
half word fetches - operand fetched as needed.

* Bit assignment is theoretical. In practice I used array indices 5 through 8 to hold the flag values.

Bus widths:
Data – 8-bits
Address – 8-bits
Control - 2-bits (one R/W bit, one memory/IO bit)

Memory configuration - 8x256

8CM Instruction Set

Instructions are in either one address or no address formats. When register addressing modes are used bit 7 becomes the operand, saving an additional fetch.

The 32 instructions in the J8CM instruction set are listed by type in the tables that follow. Tables list the instruction, the machine language code for the instruction, and the number of operand.

Data Transfer Instructions
Instruction	ML	Op	Instruction	ML	Op
INPUT	0	1	STORE ACCUM	5	1
OUTPUT	1	1	STORE X REG	21	1
LOAD ACCUM	4	1	STORE Y REG	22	1
LOAD X REG	19	1	PUSH	17	0
LOAD Y REG	20	1	POP	18	0

Arithmetic/Logic
Instruction	ML	Op	Instruction	ML	Op
ADD	2	1	ROTATE LEFT	23	0
SUBTRACT	3	1	ROTATE RIGHT	24	0
INCREMENT	10	0	AND	25	1
DECREMENT	11	0	OR	26	1
LOG SHIFT RIGHT	14	0	XOR	27	1
ARITHMETIC SHIFT LEFT	15	0	NOT	28	1
ARITHMETIC SHIFT RIGHT	16	0

 Control
Instruction	ML	Op	Instruction	ML	Op
JUMP	6	1	GOSUB	12	1
HALT	9	1	RETURN	13	0

Conversion
Instruction	ML	Op	Instruction	ML	Op
NEGATE	31	0	CLEAR	29	0

Conditional Instructions
Instruction	ML	Op	Instruction	ML	Op
TEST NEGATIVE	7	1	TEST ZERO	8	1
COMPARE	30	1