// j8cm_tec.doc

Technical information on J8CM.

MAR - Memory Address Register

PSW - Processor Status Word
  The PSW consists of four flags:
c_flag - Cycle flag. Set to zero after a fetch cycle is completed.
Set to one after an execute cycle is completed. Initially
the cycle flag is undefined and is not displayed on the
front panel. The cycle indicator display is driven by
the cycle flag.
v_flag - Overflow flag. Not used.
n_flag - Negative flag. The n-flag is set to one when bit 8 of the
accumulator is set to one.
z_flag - Zero flag. The z_flag is set to one when the contents of
the accumulator equals zero.

XREG/YREG
  General purpose ALU registers.

Memory addressing modes supported:
Memory Direct.

The Instruction Cycle
  16 bit word - 8-bit instruction, 8-bit operand.
  half word fetches

Bus widths:
  Data - 8-bits
  Address - 8-bits
  Control - 2-bits (one R/W bit, one memory/IO bit)

Memory configuration - 8x256